## Slide 1: Solar Harvest Educational Kit S4-6
Kit 2 Performance of Solar Panels

## Slide 2: Typical Types of Solar Panels
3 common types of solar panels made of silicon-based materials
Monocrystalline
A single, continuous and unbroken crystal
Polycrystalline
Composite of crystal grains
Amorphous Silicon
Disordered structure
They were introduced in Kit 1.4!

## Slide 3: Learning Objectives
Factors affecting the output power of solar panels
Paving the way for the analysis on the performance of solar panels in Kit 4
Discussion and experiments:
Effect of Distance on Illuminance
Effect of Illuminance on Output Power of Solar Panels
Effect of Incident Angle on Illuminance
Effect of EM Wavebands & Different Types of Solar Panels
Video: https://youtu.be/i5g3Kn0TMoU
More about Solar Harvest: https://re.emsd.gov.hk/english/gen/4S/4S.html

## Slide 4: Kit 2.1 Effect of Distance on Illuminance
Illuminance of a surface at different distances

## Slide 5: Inverse Square Law
Illuminance is the light power received per unit surface area
At a larger distance from the light source, light energy is distributed over a larger area, and hence the illuminance decreases
Hence at distance , the Illuminance is inversely proportional to the area of the sphere, obeying the inverse square law:
point light
source
spherical surface on which illuminance is measured (with radius )

## Slide 6: Fair Test
Study the effect of ONE factor (independent variable) at a time
Keep all other factors (control variables) the same
Compare the outcome (dependent variable)
Dependent Variable | Illuminance
Independent Variable | Distance from light source
Control Variables | Intensity of light source
 | Angle of incident light

## Slide 7: Experimental Setup
Two smartphones fixed on stands, freely movable between two metre rules
A smartphone serves as a light source using its backlight
Another smartphone with a suitable app (e.g., Phyphox) serves as a light meter
Measure illuminance at different distances

## Slide 8: Experimental Skills
Light source and light meter must be carefully aligned
Background light is subtracted from the total illuminance to obtain the illuminance of direct light
In each measurement, cardboard is used to block the direct light from the LED, and the background light is measured

## Slide 9: Experimental Results
Illuminance plotted vs 1/2 gives a straight line passing through the origin
, inverse square law verified
Distance (m) | 1/2 (m-2) | Total illuminance (lx) | Background (lx) |  | Direct illuminance (lx) | 
0.2 | 25.00 | 1100 | - | 13 | = | 1087
0.3 | 11.11 | 432 | - | 21 | = | 411
0.4 | 6.25 | 229 | - | 21 | = | 208
0.6 | 2.78 | 100 | - | 25 | = | 75
0.8 | 1.56 | 65 | - | 26 | = | 39
1.0 | 1.00 | 47 | - | 25 | = | 22
 |  | Total illuminance (lx) | Background (lx) |  |  | 
0.2 | 25.00 | 1100 | - | 13 | = | 1087
0.3 | 11.11 | 432 | - | 21 | = | 411
0.4 | 6.25 | 229 | - | 21 | = | 208
0.6 | 2.78 | 100 | - | 25 | = | 75
0.8 | 1.56 | 65 | - | 26 | = | 39
1.0 | 1.00 | 47 | - | 25 | = | 22
Chart: Direct Illuminance 𝐸 versus 1/𝑟2
| 24.999999999999996 | 11.111111111111111 | 6.2499999999999991 | 2.7777777777777777 | 1.5624999999999998 | 1
 | 1087 | 411 | 208 | 75 | 39 | 22

## Slide 10: Enrichment
Small variations in the distance between the Earth and the Sun would not affect the performance of solar panels on Earth
Effect becomes more significant when space probes visit other planets
Perihelion
Aphelion
Mars Lander (NASA/JPL-Caltech)

## Slide 11: Discussion
What are the independent variable, control variables and dependent variable in this experiment?
What is the purpose of measuring the background brightness in each measurement?
What graph should be plotted to verify the inverse square relationship between the illuminance and distance?
Explain physically why the illuminance obeys the inverse square law.
Would the change in distance affect the performance of solar panels on Earth? Under what situations would the effect be significant?

## Slide 12: Kit 2.2 Effect of Illuminance on Output Power of Solar Panels
Output power of solar panels under different illuminances

## Slide 13: Experiment
Light meter (smartphone) placed aside a solar panel under a spotlight of adjustable intensity
Adjust the intensity of the spotlight Measure illuminance with the light meter Measure current and voltage across the resistor Calculate the output power of the solar panel by
Plot the output power versus the illuminance
Does the output power of solar panels increase indefinitely with illuminance?

## Slide 14: Fair Test
Study the effect of ONE factor (independent variable) at a time
Keep all other factors (control variables) the same
Compare the outcome (dependent variable)
Dependent Variable | Output power of solar panel
Independent Variable | Illuminance
Control Variables | Distance from light source
 | Angle of incident light
 | Circuit connected to solar panel

## Slide 15: Experimental Results
Illuminance (lx) | Current ((mA) | Voltage (V) | Output power 𝑃 (mW)
14600 | 7.64 | 1.54 | 11.8
30000 | 15.1 | 3.03 | 45.8
42600 | 20.4 | 4.09 | 83.4
59500 | 26.8 | 5.37 | 144
82600 | 31.9 | 6.38 | 204
113000 | 33.4 | 6.67 | 223
136000 | 34.0 | 6.79 | 231
160000 | 34.4 | 6.87 | 236
 |  |  | Output power 𝑃 (mW)
14600 | 7.64 | 1.54 | 11.8
30000 | 15.1 | 3.03 | 45.8
42600 | 20.4 | 4.09 | 83.4
59500 | 26.8 | 5.37 | 144
82600 | 31.9 | 6.38 | 204
113000 | 33.4 | 6.67 | 223
136000 | 34.0 | 6.79 | 231
160000 | 34.4 | 6.87 | 236
Chart: Output Power 𝑃 versus Illuminance 𝐸
| 14600 | 30000 | 42600 | 59500 | 82600 | 113000 | 136000 | 160000
 | 11.4 | 45.3 | 83.6 | 145 | 204 | 224 | 231 | 237
Solar panel reaches a limit at a certain level of illuminance

## Slide 16: Discussion
What are the independent variable, control variables and dependent variable in this experiment?
How does the output power of the solar panel vary with illuminance (i) at low illuminances and (ii) at very high illuminances?
Based on the result, briefly discuss the effect of weather on the output power of solar panels. (To be further discussed in Kit 4.3)

## Slide 17: Kit 2.3 Effect of Incident Angle on Illuminance
Effect of incident angle on the illuminance (Lambert’s cosine law)

## Slide 18: Effect of the Angle of Incidence
Same amount of light is distributed over a larger area
Angle of incidence increases
Angle of incidence 𝜃 increases
Same amount of light distributed over a larger area (area increased by a factor 1/cos )
Same amount of light distributed over a larger area (area increased by a factor 1/cos 𝜃)
Illuminance decreases with cos
Illuminance 𝐸 decreases with cos 𝜃

## Slide 19: Lambert’s Cosine Law
Lambert’s cosine law: = illuminance at angle of incidence = illuminance at normal incidence
With known , calculate values of at different in theory, compare with experimental values of

## Slide 20: Experiment
Fixed smartphone (as a light meter) measures illuminance
Another smartphone (as a light source) fixed on a metal arm that can be rotated about the light meter
Angle of incidence measured by protractor
Plot illuminance vs angle of incidence , compare experimental results with theory
smartphone
(as light source)
smartphone
(as light meter)
Protractor

## Slide 21: Fair Test
Study the effect of ONE factor (independent variable) at a time
Keep all other factors (control variables) the same
Compare the outcome (dependent variable)
Dependent Variable | Illuminance
Independent Variable | Angle of incident light
Control Variables | Distance from light source
 | Intensity of light source

## Slide 22: Experimental Results
Incident angle |  | Illuminance (lx) |  | Percentage error
 |  | Measured value | Theoretical value | 
0˚ | 1 | 510 | - | -
10˚ | 0.98 | 505 | 502.25 | 0.54%
20˚ | 0.94 | 484 | 479.24 | 0.93%
30˚ | 0.87 | 450 | 441.67 | 1.63%
40˚ | 0.77 | 398 | 390.68 | 1.43%
50˚ | 0.64 | 301 | 327.82 | 5.26%
60˚ | 0.50 | 111 | 255.00 | 28.24%
 |  |  |  | Percentage error
 |  | Measured value | Theoretical value | 
0˚ | 1 | 510 | - | -
10˚ | 0.98 | 505 | 502.25 | 0.54%
20˚ | 0.94 | 484 | 479.24 | 0.93%
30˚ | 0.87 | 450 | 441.67 | 1.63%
40˚ | 0.77 | 398 | 390.68 | 1.43%
50˚ | 0.64 | 301 | 327.82 | 5.26%
60˚ | 0.50 | 111 | 255.00 | 28.24%
Chart: Illuminance 𝐸 versus Angle of Incidence 𝜃
| 0 | 10 | 20 | 30 | 40 | 50 | 60
measured value | 510 | 505 | 484 | 450 | 398 | 301 | 111
theroretical value | 510 | 502 | 479 | 442 | 391 | 328 | 255
Results agree well with Lambert’s cosine law at small angles
For large angles, reflection of light by smartphone screen affects the results

## Slide 23: Discussion
What are the independent variable, control variables and dependent variable in this experiment?
What does Lambert’s cosine law say about the relationship between illuminance and the angle of incidence? Briefly explain this relationship in terms of the distribution of light energy.
Why does the measured illuminance deviate from Lambert’s cosine law at large angles of incidence?
Give TWO factors that affect the angle of incidence of sunlight falling on a solar panel. (To be further discussed in Kit 4.1)

## Slide 24: Kit 2.4 Effect of EM Wavebands & Different Types of Solar Panels
Performance of different solar panels under different EM wavebands

## Slide 25: Radiations from the Sun
Sunlight reaching the ground contains
Infrared (IR)
Visible light
Ultraviolet (UV)
Use different light sources for the experiment
IR lamp
visible light
UV lamp

## Slide 26: Experiment
Two multimeters measure current and voltage across the resistor
Compare performance of the three types of solar panels under each EM waveband
IR
visible light
UV
monocrystalline
polycrystalline
amorphous
silicon
solar panel
ammeter
voltmeter
resistor

## Slide 27: Fair Test
Study the effect of ONE factor (independent variable) at a time
Keep all other factors (control variables) the same
Compare the outcome (dependent variable)
Dependent Variable | Output power of solar panel
Independent Variable | Type of solar panel
Control Variables | Distance between solar panel and light source
 | Intensity of each light source
 | Surface area of solar panel
 | Circuit connected to solar panel

## Slide 28: Experimental Results
IR |  |  | 
 | Amorphous silicon | Polycrystalline | Monocrystalline
Current (mA) | 0.35 | 30.3 | 31.7
Voltage (V) | 0.073 | 6.06 | 6.35
Power (mW) | 0.026 | 184 | 201
IR |  |  | 
 | Amorphous silicon | Polycrystalline | Monocrystalline
 | 0.35 | 30.3 | 31.7
 | 0.073 | 6.06 | 6.35
 | 0.026 | 184 | 201
Visible Light |  |  | 
 | Amorphous silicon | Polycrystalline | Monocrystalline
Current (mA) | 21.9 | 31.4 | 32.0
Voltage (V) | 4.38 | 6.28 | 6.40
Power (mW) | 95.9 | 197 | 205
Visible Light |  |  | 
 | Amorphous silicon | Polycrystalline | Monocrystalline
 | 21.9 | 31.4 | 32.0
 | 4.38 | 6.28 | 6.40
 | 95.9 | 197 | 205
UV |  |  | 
 | Amorphous silicon | Polycrystalline | Monocrystalline
Current (mA) | 0.33 | 3.78 | 5.60
Voltage (V) | 0.066 | 0.760 | 1.12
Power (mW) | 0.022 | 2.87 | 6.27
UV |  |  | 
 | Amorphous silicon | Polycrystalline | Monocrystalline
 | 0.33 | 3.78 | 5.60
 | 0.066 | 0.760 | 1.12
 | 0.022 | 2.87 | 6.27
Output power: Monocrystalline > Polycrystalline > Amorphous silicon
Monocrystalline solar panels perform best
  Widely used on permanent facilities
  Monocrystalline solar panels are installed under the Solar Harvest scheme

## Slide 29: Remark
Output power of light sources (IR, visible light, UV) are different: CANNOT compare the performance of the same solar panel under different wavebands
Can compare the performance of 3 types of solar panels under each waveband only
IR lamp
visible light
UV lamp

## Slide 30: Discussion
What are the independent variable, control variables and dependent variable in this experiment?
Which of the three types of solar panels is best performing under all three different wavebands?
Why are the results under the three sources not comparable? Despite this, to which waveband are the solar panels least responsive?

## Slide 31: Conclusion
Illuminance is lower at larger distance from light source (insignificant for solar panels on Earth surface)
Output power does not increase indefinitely with illuminance, it approaches a maximum value beyond a certain illuminance
Lambert’s cosine law tells us how the Illuminance decreases with larger angles of incidence
Monocrystalline solar panels are more efficient than polycrystalline and amorphous silicon ones under IR, visible light and UV
Performance of solar panels is affected by many factors

## Slide 32
End of Kit 2