## Slide 1: Solar Harvest Educational Kit S4-6
Kit 4 Seasonal Changes & Solar Energy

## Slide 2: Solar Harvest
Solar Harvest is a Government programme which aims to promote the development of renewable energy in Hong Kong.
It provides financial and technical support for eligible schools & welfare NGOs to install solar energy generation systems at their premises.
It also assists in joining the Feed-in Tariff (FiT) Scheme. The income can be used for maintenance, education and welfare services.

## Slide 3: Real-time Monitoring System (RTMS)
Real-time Monitoring System (RTMS) monitors the solar irradiance and output power
It also shows other data, such as total amount of carbon emission reduced
Long-term data are stored online and downloadable for analysis

## Slide 4: RTMS Interface
Date & time
Solar irradiance
Daily output energy
Monthly output energy
Total output energy since installation
Graph of real-time data

## Slide 5: Data Download
Step 1: Click the button
Step 2: Choose the desired period and click “Submit”
Step 3: Click the “Data view” button
Step 4: Export the data to Excel file

## Slide 6: Illuminance VS Irradiance
Illuminance（光照度）
Power of visible light incident per unit area, corrected for the sensitivity of eye to different wavelengths
Unit: lux (lx)
Power of radiation energy (including visible light, UV & IR) incident per unit area
Unit: W m-2
Irradiance（輻照度）

## Slide 7: Learning Objectives
Analysis of data from RTMS and Hong Kong Observatory (HKO)
Other factors affecting the performance of solar panels (e.g., weather, seasons)
Discussion and experiments:
Daily & Seasonal Changes
Solar Spectrum
Effect of Weather
Design of Solar Energy Generation Systems
Video: https://youtu.be/B5GItfi_RF4
More about Solar Harvest: https://re.emsd.gov.hk/english/gen/4S/4S.html

## Slide 8: Kit 4.1 Daily & Seasonal Changes
Effect of daily and seasonal variations on solar panels

## Slide 9: Selection of Date for Daily Variation
Look up the past weather data from HKO (https://www.hko.gov.hk/tc/cis/dailyElement.htm)
To avoid the effects of weather, choose a date with low cloud amount and high solar radiation
Download RTMS data, plot output power & solar irradiance vs time
Date chosen in the video:
13 September 2022 | 
Cloud Amount | 5%
Sunshine Duration | 11.0 hours
Daily Yield | 65.25 kWh
Chart: Power Output & Solar Irradiance

## Slide 10: Performance over a Day
Recall Lambert’s cosine law (Kit 2.3)
Morning/evening: Large angles of incidence of sunlight  low solar irradiance & output power
At noon: Small angles of incidence of sunlight  High solar irradiance & output power
Curve of output power changes in steps: Averaged values in 15-minute intervals
Chart: Power Output & Solar Irradiance

## Slide 11: Geographical & Seasonal Effects
Performance of solar panels depends on:
Latitude of installation: The equator receives more sunlight than high latitudes
Seasonal variations: Sun higher in the sky & longer sunshine duration in summer
Equator
N
S
Summer in the Northern Hemisphere
23.5°

## Slide 12: The Cause of Seasons
Axis of rotation
23.5°
Axis of Earth rotation inclined by about 23.5° (from the direction perpendicular to the Earth’s orbit)

## Slide 13: Vernal & Autumnal Equinoxes
Vernal Equinox
Around 21 March (spring in the Northern Hemisphere)
Sunlight shines on the equator directly
The equator receives more sunlight
Around 21 September (autumn in the Northern Hemisphere)
Sunlight shines on the equator directly
The equator receives more sunlight
Autumnal Equinox
Equator
Equator

## Slide 14: Summer & Winter Solstices
Sunlight shines on the Tropic of Cancer directly
The Northern Hemisphere receives more sunlight than the Southern Hemisphere
Sunlight shines on the Tropic of Capricorn directly
The Northern Hemisphere receives less sunlight than the Southern Hemisphere
Tropic of Cancer
Summer Solstice
Around 21 June (summer in the Northern Hemisphere)
Winter Solstice
Around 22 December (winter in the Northern Hemisphere)
Tropic of Capricorn

## Slide 15: Sun Paths in HK
Summer in HK
Sun directly overhead (small incident angles)  Higher irradiance & output power
Longer sunshine duration (about 14 hours in HK)  Higher yield
Sun lower in the sky (large incident angles)  Lower irradiance & output power
Shorter sunshine duration (about 10 hours in HK)  Lower yield
Winter in HK

## Slide 16: Selection of Dates for Seasonal Variations
Choose a date near the summer solstice & a date near the winter solstice
To reduce the effects of weather, the cloud amount of the two dates should be similar Past weather data from HKO (https://www.hko.gov.hk/tc/cis/dailyElement.htm)
Download RTMS data on those days, plot the output power and solar irradiance vs time
Dates chosen in the video:
 | 24 June 2022 (Summer) | 25 December 2021 (Winter)
Cloud Amount (%) | 63 | 66
Sunshine Duration (hours ) | 13.50 | 10.78
Daily Yield (kWh) | 49.00 | 29.75

## Slide 17: Comparison of Summer & Winter
Chart: Output Power
Chart: Solar Irradiance
sunrise
sunset
Summer (Red curve): Higher solar irradiance & output power, longer sunshine duration
Winter (Blue curve): Lower solar irradiance & output power, shorter sunshine duration

## Slide 18: Discussion
In the RTMS data analysis for daily variations, why is it important to select a sunny day?
Explain the variations of solar irradiance and output power of solar panels over a day.
What causes the seasons on Earth? Explain the features of the vernal equinox, summer solstice, autumnal equinox and winter solstice.
When studying seasonal effects, why is it important to compare two days with similar cloud amounts?
Which season does the solar panels perform better? List TWO reasons for the observation.

## Slide 19: Kit 4.2 Solar Spectrum
Observing the composition of sunlight

## Slide 20: Spectrometry
Spectrum: A graph showing the intensity of different wavelengths
Measure spectra of the Sun and the clear sky by a portable spectrometer with an optical fibre
Mobile app interface displays the spectrum
Compare spectra of the clear sky and the Sun
portable spectrometer
optical fibre

## Slide 21: Experimental Results
Spectrum of the clear sky
Peak at about 500 nm (blue)
Sunlight scattered by the atmosphere
Blue light scattered more  Blue sky
Spectrum of the Sun
Peaks at about 600 nm (yellow-green)
Hot enough to emit light as a blackbody; colour related to the temperature
Surface temperature of the Sun: 5800 K

## Slide 22: Solar Spectra on Ground & in Space
Irradiance on Earth’s surface is lower because the atmosphere absorbs and reflects part of the sunlight
Abrupt drops in intensity in the IR region are due to the absorption by water vapour
Absorption of IR by greenhouse gases (e.g., carbon dioxide) leads to the greenhouse effect

## Slide 23: Discussion
Explain the differences between the spectra of direct sunlight and the clear sky.
Explain the differences between the solar spectra measured in space and on the ground.
Relate the observations in the IR region of solar spectrum measured on the ground to greenhouse effect.

## Slide 24: Kit 4.3 Effect of Weather
Discussion on the effect of weather on solar panels

## Slide 25: Selection of Dates
Look up the past weather data from HKO (https://www.hko.gov.hk/tc/cis/dailyElement.htm)
Choose a date with a low cloud amount (sunny) & another date with a high cloud amount (cloudy)
To reduce seasonal effects, the two dates should be close to each other
Download RTMS data on those days, plot output power & solar irradiance vs time
Dates chosen in the video:
 | 1 April 2022 (cloudy) | 4 April 2022 (sunny)
Cloud Amount (%) | 90 | 5
Daily Yield (kWh) | 19.00 | 78.50

## Slide 26: Comparison of Sunny & Cloudy Days
Sunny day (Green curves)
Higher solar irradiance and output power
Smoother curves
Cloudy day (Brown curves)
Lower solar irradiance and output power
Blocking of sunlight by cloud  Rougher curves
Chart: Solar Irradiance
Chart: Output Power

## Slide 27: Scattering of Sunlight
Clouds can scatter sunlight into different directions. Solar panels can absorb scattered light and generate electricity.
How could solar panels manage to generate electricity in cloudy days?
Certainly, scattered sunlight has a lower intensity than direct sunlight. The solar irradiance and output power are lower on cloudy days.

## Slide 28: Long-term Observation
Monthly data over a year observed (Cloud amount data obtained from HKO)
Cloudy months  lower solar irradiance & output power
Weather dominant over seasonal factor
Chart: Average Output Power & Average Cloud Amount
| JAN | FEB | MAR | APR | MAY | JUN | JUL | AUG | SEP | OCT | NOV | DEC
average output power | 3.6624 | 3.8806 | 4.4291 | 5.0386 | 3.8618 | 3.9084 | 4.5859 | 4.2544 | 5.2305 | 5.286 | 3.1599 | 4.9136
average cloud amount | 67.0645 | 76.8214 | 63.9677 | 57.8 | 81.7742 | 82.7333 | 60.6774 | 70.7097 | 53.5333 | 55.5806 | 71.2 | 51

## Slide 29: Discussion
In the comparison, why is it important to choose the sunny day and the cloudy day close to each other?
Why do the solar irradiance and output power curves fluctuate on the cloudy day?
Why can solar panels generate electricity even under very cloudy weather?
How is the long-term variation of output power related to weather?
The graph shows that the solar panels did not perform best during summer. What is the possible reason?

## Slide 30: Kit 4.4 Design of Solar Energy Generation Systems
Qualitative discussion on the adaptive designs of solar panels in Hong Kong

## Slide 31: Inclination of Solar Panels
Is there any adaptive method to improve the performance of solar panels?
The latitude of Hong Kong is 22.5°N. For most of the time in a year, the Sun is due South at noon.
Solar panels installed by the Solar Harvest scheme are inclined by 14° toward the South.
Heavy load
Wind blowing over the rooftop
Why don’t we incline them by 22.5°?
With a smaller inclination angle, solar panels will not be easily blown away by strong winds (e.g., typhoons and strong monsoons), so less load is needed to stabilize the solar panels.

## Slide 32: Solar Panels with Sun-tracking Devices
Some solar panels are equipped with sun-tracking devices
Motor turns the solar panel towards the Sun over a day
Maintain small angles of incidence, larger output power
A solar panel with sun-tracking device

## Slide 33: Better Land Use
Land is limited in Hong Kong
Solar panels built on floating platforms on reservoirs makes better land use
Extra benefit: Reduce sunshine on the reservoir and water loss by evaporation
Floating solar panels on reservoir

## Slide 34: Discussion
Why are the solar panels in Hong Kong inclined to the South? Why is the angle of inclination smaller than the latitude of Hong Kong?
How does the sun-tracking devices improve the performance of solar panels?
What are the advantages of building solar panels in remote areas, such as reservoirs?

## Slide 35: Conclusion
Factors affecting the incident angle of sunlight: the Sun’s position in the sky over a day, and the sun paths in different seasons
Composition of sunlight can be studied by spectrometry: absorptions by the atmosphere are observed at some wavelengths
In the long term, the effect of weather on the performance of solar panels dominates that of seasonal variations
Adaptive designs can improve the efficiency of solar energy generation systems
RTMS is useful for observing the factors that affect the performance of solar panels.

## Slide 36
End of Kit 4